## Slide 1
S.L.O.S.H. - System for Liquid Orbital Supply and Handling
A. Alexy, J. Broussard, A. Dean, D. Garceau, J. Grady, B. Kerridge,
B. Smucker, R. Wagner, C. Zelasko
Faculty Advisor: Dr. Daniel R. Kirk, Dept. of Aerospace, Physics, and Space Sciences,
Florida Institute of Technology
What Did We Learn?
‘Sponge’ - retains propellant within 6cm diameter under accelerations
Anti-Vortex Device - mitigates vortices and vapor ingestion
7.7cm
Modular Outlet - can change components in/out
LOX Propellant Management Device (PMD) Design
Conclusions
PMD shows significant improvement for drain angles 0°-25°
PMD components successfully mitigated vortices, reducing residual fluid levels
Loss in flow rate while testing PMD was within acceptable limits
Testing & Equipment
Gimbaling Apparatus
Rotating Apparatus
Why Manage Propellants in Microgravity?
Deep space missions start with mastering in-orbit propellant transfer
In microgravity, liquid propellants don’t settle–they float
Vapor leads to system failure, engines demand pure liquid
Project Objectives
Design Propellant Management Device to handle Liquid Oxygen (LOX)
Develop equipment to simulate operating conditions
Conduct quantitative tests using cryogenic simulant (water)
Evaluate/Analyze device performance
Florida Tech SPHERES Experiment
10° no PMD
10° with PMD
1.02 m
1.81 m
9cm
4.32cm
Notes: 1.81 mm