## Slide 1
Sustainable Acetylene Synthesis (SAS)
Taylor Disharoon, Gene Koifman, Erik Laari, Isabella Luznar
Faculty Advisor: Dr. Jonathan E. Whitlow, Dept. of Chemistry and Chemical Engineering, Florida Institute of Technology
Abstract
Process Flow Diagram
PFD Table Index
Economics and Profitability
Novelty
Reactions
Process Specifications
Sustainable acetylene production process using CO2 from flue gas, CaO, and water, with an innovative approach to carbon capture and high-purity acetylene generation, supporting industrial demand and reducing greenhouse gas emissions.
Plant located in Tatum, Texas
Capital cost of $75 million
Annual manufacturing cost of $158 million
Net profit of $923 million after 2 years of construction and 10 years of production
Internal Rate of Return on Investment of 52%
Breakeven point after 3 years
4,300 kmol/hr CO2 captured from flue gas
1,400 kmol/hr pure acetylene produced
Raw material cost is $66 million
The process captures CO2 from flue gas using MEA absorption, converting waste emissions from coal plants into acetylene feedstocks.
Electrochemical reduction of CO2 in a molten salt reactor produces calcium carbide, which is hydrolyzed to generate high-purity acetylene.
Carbon Capture:
MEA + CO2  (R-NH-COO)- + H+
(R-NH-COO)- + H+  MEA + CO2
Acetylene Synthesis:
2CO2 (g) + CaO (l)  CaC2 (s) + 2.5O2 (g)
CaC2 (s) + H2O (l)  C2H2 (g) + Ca(OH)2 (aq)